## Slide 1: SOCKET COMMUNICATION

## Slide 2: Socket Communication in Cavli Cellular Modules
•Cavli Wireless modules (e.g., C10GS, C42QM) support TCP/IP stack.
•Common use case: Cloud data push via TCP sockets.
•Commands: AT+QIOPEN (open connection), AT+QISEND (send data)

## Slide 3: Setup & Prerequisites
•**Set PDP Context**
•AT+CGDCONT=1,"IP","<APN>"
•
•**Activate PDP**
•AT+QIACT=1
•
•**Verify Registration**
•AT+CGREG? / AT+CEREG?

## Slide 4: AT+QIOPEN – Open TCP Socket
•**Syntax:**
•AT+QIOPEN=<ctx_id>,<conn_id>,"TCP","<IP>",<port>,<lport>,<mode>
•
•**Example:**
•AT+QIOPEN=1,0,"TCP","220.180.239.212",8009,0,1
•
•**Expected Response:**
•OK
•+QIOPEN: 0,0 (Success)

## Slide 5: AT+QISEND – Send TCP Data
•**Syntax:**
•AT+QISEND=<conn_id>,<length>
•
•**Send Flow:**
•AT+QISEND=0,12
•> Hello World!
•[Ctrl+Z]
•
•**Response:**
•SEND OK

## Slide 6: Receiving Data
•**URC Indication (Buffer Mode):**
•+QIURC: "recv",0
•
•**To Read Buffer:**
•AT+QIRD=0,1500
•
•**Direct Mode:**
•+QIURC: "recv",0,12
•Hello World!

## Slide 7: Closing the Socket
•Close connection:
•AT+QICLOSE=0
•
•Deactivate PDP:
•AT+QIDEACT=1

## Slide 8: Full Example Workflow
•1. AT+CGDCONT=1,"IP","apn"
•2. AT+QIACT=1
•3. AT+QIOPEN=1,0,"TCP","1.2.3.4",80,0,1
•4. AT+QISEND=0,13
•5. > Hello World!
•6. AT+QICLOSE=0
•7. AT+QIDEACT=1

## Slide 9: Tips & Considerations
•- Always wait for +QIOPEN and +QIURC responses.
•- Ensure context is activated before QIOPEN.
•- Use AT+QISTATE to check socket state.